# Assembling The Quirkey V3
## Overview
The basic Quirkey chord keyboard consists of 6 microswitches fitted with keycaps on a base, covered with a shell, powered by a single micro controller board and connected via a USB cable. The default firmware emulates a full standard US USB keyboard, but the code can be reconfigured to other languages. No driver is needed on the PC, laptop, tablet etc.
Supported controllers are currently an Arduino-compatible that supports the USB HID interface (such as the Leonardo Mini), and Raspberry Pi Pico variants.
## Components List
The following items are needed for assembly:
AT32U4-based Arduino
OR
Raspberry Pi Pico with USB
USB Lead to suit the above, 1m+
6 miniature lever microswitches
5 keycaps, thumb key, command key, shell, base (3D printed)
~1.5m thin PVC insulated stranded wire
Solder
4 countersunk woodscrews 6g x 12-16mm
4 Stick-on non-slip pads or foam tape
Small cable tie
Suggested Tools
Sidecutters
Wire stripping tool of choice
Needle nosed pliers
Soldering iron and sponge
Screwdriver to fit screws
## Program The Controller Firmware
You will find the code on https://github.com/VikOlliver with the Arduino code under ‘Microwriter’ and the CircuitPython code under ‘Quirkey’. The controllers are programmed with their respective standard environments using the USB lead, so rather than reproduce the fine details here, refer if necessary to the README on GitHub and either http://arduino.cc or http://circuitpython.org
Note: When plugging in and unplugging the controller always hold the USB socket between finger and thumb. Do not hold the board itself, otherwise you will snap the USB socket off! (Ask us how we know)
## Wire The Microswitches
Cut 7	lengths of wire 120mm long, 4 lengths 90mm long, and one 40mm long. Strip about 8mm off each end. Connect the 40mm length to a 90mm length by twisting the ends together. In the same way, connect the 3 remaining 90mm lengths together in a row, and twist a 120mm length onto one end. Twist all the remaining free ends to prevent fraying.
Tin all the twisted ends well with solder – solder should cover all the wire surface and hold the twists firmly in a lump. Trim all the ends and twists to 4mm.
Identify the “NO” and “C” contacts on the microswitch (these are the two that join together when the switch is depressed). Tin these terminals of the microswitches so that each terminal is topped by a small blob of solder.
Solder every twisted wire joint to the “NO” pin of its own microswitch. Solder another microswitch’s “NO” pin to the end of the short wire. Solder the last microswitch to the free end of the 90mm wire. the You should now have a chain of two switches with a long free wire on it, and a chain of four switches with a free wire on it. Mark these wires in some way to avoid confusion later. Now solder a 120mm wire to the “C” pin of every microswitch.
## Solder The Switches To The Controller
When connecting the wires to the controller, insert the wire from the underside of the board. It is good practice to ensure the insulation of each wire is right against the board so that no bare wire is exposed. Solder both marked wires to any convenient GND hole on the controller.
Solder the remaining microswitch wires to controller IO pads as follows for both Arduino and a standard Pi Pico:
Switch	Inner	Pinkie	Ring	Middle	1st	Thumb
Pin D/GP	8	7	6	5	4	9
Character	SHIFT	u	s	o	e	SPACE

## Fit Microswitches
The microswitches are placed in the sockets of the base pillars with the free ends of their levers pointing to the front (rounded end) of the base. The levers go on the top! There are vertical slots in the sides of the pillars to let the wires out.
Start with the string of two microswitches. Put the microswitch with two wires attached in the leftmost socket on the “thumb” pillar, trailing its wires through the slot towards the pillar to its right. Put the other microswitch in the inner socket next to it.
Put the remaining four microswitches in sequence in the “finger” pillars, using the sequence detailed in the soldering instructions.
Trim excess wire from joints. Carefully plug the USB lead into the controller. If using a Pi Pico, there are pillars on the base on which the board can be impaled, component side down with the USB socket on the right.
Generously curve the USB cable in an ‘S’ shape, avoiding sharp turns, and push it into the cable slot on the right side of the base. On the inside part of the cable, firmly attach a cable tie to prevent the cable being pulled through from the outside. Trim off excess tie.
## Fit The Keycaps
The small keycap with a hole in the bottom should be a snap fit onto the peg on the double-sized key, but feel free to add a small dot of superglue in the hole. Make sure the finger ridges in the top point in the same direction. All finger ridges have the rounded end of the ridge pointing to the front.
Do not just push the double key into the thumb socket. The forward pivot is hooked into the forward hole in the double pillar, then the rear pivot is snapped into place (some ‘O’-ring lubricant on the pivots and projections is a good idea).
If using multi-coloured keycaps, snap them into place in the following order, which is the order used in the tutorial and documentation:

Switch	Pinkie	Ring	Middle	1st
Colour	Blue	Green	Yellow	Orange

## Adding The Shell
Lower the shell onto the base. It is best to aim to get the double key into its hole first, then wriggle it down. You may need to push down on some keys to provide enough clearance.
Drive a screw into each of the countersunk holes. Barely tighten them all at first, then tighten more firmly. It is best to just tighten the screws enough to stop the base moving. Do not crank on them until they squeak and add a quarter turn.
Stick the 4 non-slip pads (or foam tape strips) to the base of the Quirkey, spacing things out for maximum stability – the exact position may vary between users.
## You’re Finished!
Congratulations, you can now start typing with your Quirkey. Share and enjoy.
This document is ©2023 by Vik Olliver vik@diamondage.co.nz and may be freely shared under the terms of the GFDL V1.3 or later version. In the event of a licence conflict, please contact the author.