# Assembling V4
## Overview
The basic Quirkey chord keyboard consists of 6 keyswitches fitted with keycaps on a base, covered with a shell, powered by a single micro controller board and connected via a USB cable. The default firmware emulates a full standard US USB keyboard, but the code can be reconfigured to other languages. No driver is needed on the PC, laptop, tablet, phone etc.
Supported controllers are currently an Arduino-compatible that supports the USB HID interface (such as the Leonardo Mini), and Raspberry Pi Pico variants.
## Components List
The following items are needed for assembly:
AT32U4-based Arduino
OR
Raspberry Pi Pico with USB
USB Lead to suit the above, 1m+
6 MX Cherry-type keyswitches
5 keycaps, 2 thumb keys, shell, base (3D printed)
~1.5m thin PVC insulated stranded wire
Solder
4 countersunk woodscrews 6g x 12-16mm
4 Stick-on non-slip pads or foam tape
Small cable tie
Suggested Tools
Sidecutters
Wire stripping tool of choice
Soldering iron and sponge
Screwdriver to fit screws
## Program The Controller Firmware
You will find the code on https://github.com/VikOlliver with the Arduino code under ‘Microwriter’ and the CircuitPython code under ‘Quirkey’. The controllers are programmed with their respective standard environments using the USB lead, so rather than reproduce the fine details here, refer if necessary to the README on GitHub and either http://arduino.cc or http://circuitpython.org
Note: When plugging in and unplugging the controller always hold the USB socket between finger and thumb. Do not hold the board itself, otherwise you will snap the USB socket off! (Ask us how we know)
## Wire The Keyswitches
Cut 7	lengths of wire 120mm long, 4 lengths 90mm long, and one 40mm long. Strip about 8mm off each end. Connect the 40mm length to a 90mm length by twisting the ends together. In the same way, connect the 3 remaining 90mm lengths together in a row, and twist a 120mm length onto one end. Twist all the remaining free ends to prevent fraying.
Tin all the twisted ends well with solder – solder should cover all the wire surface and hold the twists firmly in a lump. Trim all the ends and twists to 4mm.
Tin the terminals of the keyswitches so that each terminal is topped by a small blob of solder.
Solder every twisted wire joint to one pin of its own keyswitch. Solder another keyswitch’s pin to the end of the short wire. Solder the last keyswitch to the free end of the 90mm wire. You should now have a chain of two switches with a long free wire on it, and a chain of four switches with a free wire on it. Mark these wires in some way to avoid confusion later. Now solder a 120mm wire to the other pin of every keyswitch.
## Solder The Switches To The Controller
When connecting the wires to the controller, insert the wire from the underside of the board. It is good practice to ensure the insulation of each wire is right against the board so that no bare wire is exposed. Solder both marked wires to any convenient GND hole on the controller.
Solder the remaining keyswitch wires to controller IO pads as follows for both Arduino and a standard Pi Pico:
Switch	Inner	Pinkie	Ring	Middle	1st	Thumb
Pin D/GP	8	7	6	5	4	9
Character	SHIFT	u	s	o	e	SPACE

## Fit keyswitches
The keyswitches have four sloping sides to the top of the switch body. One side is more steeply sloped than the others. We’ll call that the “Flat” for now. There are vertical slots in the sides of the pillars to let the wires out. Make sure every keyswitch goes in straight, and is pushed down to the ledge in the cavity.
Start with the string of two keyswitches. With the Flat facing inwards, put the keyswitch with two wires attached in the outermost socket on the “thumb” pillar, trailing its wires through the slot towards the inside pillar. Put the other keyswitch in the inner socket next to it, with the Flat facing outwards. The flats on the two switches face each other if you get it right.
Put the remaining four keyswitches in sequence in the “finger” pillars, using the sequence detailed in the soldering instructions. Insert the four finger switches with the Flats facing inwards.
Trim excess wire from joints. Carefully plug the USB lead into the controller. If using a Pi Pico, there are pillars on the base on which the board can be impaled, component side down with the USB socket on the right.
Generously curve the USB cable in an ‘S’ shape, avoiding sharp turns, and push it into the cable slot on the right side of the base. On the inside part of the cable, firmly attach a cable tie to prevent the cable being pulled through from the outside. Trim off excess tie.
## Fit The Keycaps
You will notice that every keycap has a wide notch in one side. This notch goes over the Flat of the keyswitch. Push the red thumb keycap onto the outermost thumb keyswitch, and the black keycap on the innermost (if you’re using coloured keycaps).
Push the remaining 4 finger keycaps into place in the following order, which is the order used in the tutorial and documentation:

Switch	Pinkie	Ring	Middle	1st
Colour	Blue	Green	Yellow	Orange

## Adding The Shell
Check all the keycaps move without binding. Lower the shell onto the base. It is best to aim to get the thumb keys into their hole first, then wriggle it down. You may need to push down on some keys to provide enough clearance.
Drive a screw into each of the countersunk holes. Barely tighten them all at first, then tighten more firmly. It is best to just tighten the screws enough to stop the base moving. Do not crank on them until they squeak and add a quarter turn.
Stick the 4 non-slip pads (or foam tape strips) to the base of the Quirkey, spacing things out for maximum stability – the exact position may vary between users.
## You’re Finished!
Congratulations, you can now start typing with your Quirkey. Share and enjoy.
This document is ©2023 by Vik Olliver vik@diamondage.co.nz and may be freely shared under the terms of the GFDL V1.3 or later version. In the event of a licence conflict, please contact the author.